## Slide 1
Neural Network based Object Detection on PYNQ FPGA – iSmart2
Cong Hao(1), Yuhong Li(1), Sitao Huang(1), Xiaofan Zhang(1), Tianqi Gao(1),
Jinjun Xiong(2), Kyle Rupnow(3), Huafeng Yu(4), Wen-Mei Hwu(1), and Deming Chen(1&3)
(1): ECE Department, University of Illinois at Urbana-Champaign (2): IBM (3): Inspirit IoT, Inc. (4): The Boeing Company

## Slide 2
Solution Overview
Software DNN model
FPGA Implementation
  IP Design
  System Design
Experimental Results
Conclusions
Outline
http://www.pynq.io/

## Slide 3
Customized neural network model
Performance-driven model design to reduce back-and-forth efforts
Respecting FPGA resources (DSP, BRAM) and performance constraint (5FPS)
Customized FPGA implementation
  IP Design
  IP Reuse and Data Reuse
  System Optimization
Solution Overview
Neural Network Design and Training
FPGA Implementation
start
end
start
end

## Slide 4
Limited hardware resources, 5FPS speed requirement
  Light neural network
Performance-Driven Neural Network Design
  Depth-wise and Point-wise convolutional layers
  Two types of convolutional kernels (3x3 and 1x1)
Hardware friendly
  More IP reuse among layers
  Less types of kernels, less IPs
Q 1
Layer Type?
Computed from the latency constraint (5 FPS, 200ms )
  Maximum # of computations
  8 ~ 10 layers of convolutional layers, 12~14 with pooling
Q 2
Kernel Type?
Q 3
# of layers?

## Slide 5
Proposed NN model – customized from Mobilenet[1] & Yolo[2]
Relu
Relu
Relu
Relu
Relu
Relu
Relu
Relu
depth-wise 3x3 convolutional layer (mobilenet)
point-wise 1x1 convolutional layer (mobilenet)
2x2 max pooling layer
bounding box regression (Yolo)
Input Image
360*640
Resize
160*320
DW
DW
DW
DW
Output
bounding box
[x1, y1, x2, y2]
160(h)*320(w)*3(ch)
160(h)*320(w)*48(ch)
80(h)*160(w)*48(ch)
80(h)*160(w)*48(ch)
80(h)*160(w)*96(ch)
40(h)*80(w)*96(ch)
40(h)*80(w)*96(ch)
40(h)*80(w)*192(ch)
20(h)*40(w)*192(ch)
20(h)*40(w)*192(ch)
20(h)*40(w)*384(ch)
20(h)*40(w)*10(ch)
[1] Howard, Andrew G., et al. ”Mobilenets: Efficient convolutional neural networks for mobile vision applications.” arXiv preprint arXiv:1704.04861 (2017).
[2] Redmon, Joseph, and Ali Farhadi. ”YOLO9000: better, faster, stronger.” arXiv preprint (2017).
Hardware
Friendly

## Slide 6
Customized FPGA Implementation
High-Level Synthesis to generate Verilog design
Quantization: 8-bit fixed point weights, 16-bit fixed point feature map
IP Design & IP Reuse
  IPs: Conv 3x3, Conv 1x1, Max Pooling, Relu, etc. ==> one instance per IP
  One IP is reused by all the layers of the same type
Data Reuse
  IP level and feature map level
Latency Optimization
  Image and feature map partition
  Fine-grained buffer schedule and IP pipeline

## Slide 7
Depth-Wise Convolutional 3x3 IP
*
data_in1
weight1
+
data_out1
*
+
*
+
…
channel 1
channel 2
channel 15
…
accumulate
*
+
channel 16
data_out2
data_out15
data_out16
data_in2
weight2
data_in15
weight15
data_in16
weight16
Accumulate 3x3 times for one output
Parallelism: 16
Multipliers: 16
Adders: 16
DSPs: 16
…
…
di1
data in
di2
di16
…
…
w1
weight
w2
w16
16 input channels
…
…
data out
do1
do2
do16
16 output channels

## Slide 8
data in
…
+
*
PE 1
*
*
…
*
+
+
+
+
+
+
Output
Channel 1
+
*
PE 2
*
*
…
*
+
+
+
+
+
+
Output
Channel 2
+
*
PE 8
*
*
…
*
+
+
+
+
+
+
Output
Channel 8
…
kernel 1
data_out1
data_out2
data_out8
…
…
kernel 2
kernel 8
16 input channels
8 output channels
…
Parallelism: 16*8 = 128
Multipliers: 16*8 = 128
Adders: 15*8 = 120
DSPs: 16*8 = 128
Point-Wise Convolutional 1x1 IP

## Slide 9
BRAM
Overall System Diagram
Input Image 360*640
Resize to 160*320
Convert to RGB
Copy to
Depth-Wise
Conv
3x3
Bounding
Box
Regression
Image Normalization
buffer 1
buffer 2
DRAM
buffer 5
buffer 6
buffer 14
buffer 15
…
buffer 16
weight buffer 3x3
Coordinates
model weights
Image RGB data
feature map after each pooling layer
buffer 3
buffer 4
on-chip data transfer
Point-Wise
Conv
1x1
weight buffer 1x1
Max
Pooling
off-chip data transfer
PS
PL

## Slide 10
Image partition, fine grained buffer scheduling, IP pipeline
DRAM data transfer pattern
Fine Grained IP/Buffer Scheduling
Input image: cut into 8x8 slices
DRAM
BRAM
DRAM
DRAM data transfer
DRAM data transfer
1x1 CONV IP
Layer2
Feature map chunks
3x3 CONV IP
Layer1
Image chunk
POOLING IP
Layer3
Feature map chunks
3x3 CONV IP
1x1 CONV IP
POOLING IP
b6
DDR load
DDR write
1/3 Channels
b1
b3
3x3 CONV IP
DDR load
b2
b4
b5
1x1 CONV IP
POOLING IP
b6
DDR write
b5
1x1 CONV IP
POOLING IP
b6
DDR write
b5
2/3 Channels
3/3 Channels

## Slide 11
Experimental Results
NN Structure | IoU |  | Latency (ms) |  | Speed (fps) |  | Power (W) |  | Energy (Wh) |  | Resource Utilization |  |  | 
 | GPU | FPGA | 100MHz | 150MHz | 100MHz | 150MHz | 100MHz | 150MHz | 100MHz | 150MHz | LUT | BRAM | DSP | FF
12layer 64ch | 26.6% | 26.3% | 13 | -- | 20 | -- | 2.35 | -- | -- | -- | 75.7% | 77.5% | 59.7% | 15%
12layer 128ch | 38.6% | 38.9% | 34 | - | 20 | -- | 2.35 | -- | -- | -- | 76.7% | 94.3% | 76.2% | 17%
12layer 256ch | 45.6% | 45.5% | 120 | -- | 8.3 | -- | 2.35 | -- | -- | -- | 77.5% | 95.4% | 81.8% | 18%
12layer 384ch | 57.3% | 57.3% | 175 | 131 | 5.7 | 7.6 | -- | 2.59 | -- | 5.12 | 76.7% | 95.4% | 84.2% | 22%
14layer 512ch | 60.4% | 60.4% | 256 | 194 | 3.7 | 5.0 | -- | 2.82 | -- | 8.13 | 76.7% | 95.4% | 84.2% | 23%

## Slide 12
Conclusions
Final design results
  12 layers NN model with maximum 384 channels
  57.3% IoU, 7.6 FPS, 5.12 WH
  IP and buffer reuse saved FPGA resources and reduced DDR data transfer
  The more DDR data transfer, the longer latency and higher energy
  High Level Synthesis
  Provides fast prototyping and higher level design optimization